## Slide 1: Bayesian Inference in Risk Assessment (P-102)
Dr. Curtis Smith
Curtis.Smith@inl.gov
Kurt Vedros
Kurt.Vedros@inl.gov
Dr. Diego Mandelli
Diego.Mandelli@inl.gov
Course Presented by
August 8th-13th, 2019
Idaho Falls, Idaho

## Slide 2: Your Instructors
Dr. Curtis Smith
  Director for the Idaho National Laboratory Nuclear Safety and Regulatory Research Division. Lead of the Risk Informed Safety Analysis (RISA) under the DOE Light Water Reactor Sustainability Program
Dr. Diego Mandelli
  Research emphasis on PRA methodologies that combine system simulators and stochastic methods, data mining and machine learning methods
Kurt Vedros
  Research emphasis on Bayesian parameter estimation, population variability, SPAR model development in various projects, external events, and electrical grid resiliency

## Slide 3: Dedication
The “probability and stats” course was developed by Dr. Dana Kelly in the 1990s
We dedicate this course to his memory
One of Dana’s mantras (taken from the Copenhagen interpretation of quantum physics) was “Shut up and calculate!” We embrace this approach in this class…

## Slide 4: Bayesian Inference in Risk Assessment (P-102)
Section 1: Course Topics
Section 2: Review of Basic Probability Calculations
Section 3: Introduction to Bayesian Inference
Section 4: Introduction to Monte Carlo Sampling
Section 5: Uncertainty Propagation in Risk Assessment
Let us discuss the information in these sections…

## Slide 5: Section 1: Course Topics
The “stats” course, P-102, comprises three sections
  Review of basic probability calculations
    Things you should already know, so we will just remind you of them
  Basic Bayesian statistical inference
    We will use Excel to do the math
      We will demo another tool for harder problems
  Uncertainty propagation in risk assessment
    Simple Monte Carlo sampling
      Propagation of parameter uncertainty through risk model
      We will illustrate this in Excel

## Slide 6: Section 2: Review of Probability
Purpose
  Students will review probability axioms and operations
Objectives
  Students will be able to calculate results involving
    “AND”, “OR”, “NOT” operations
    Conditional probabilities
    Bayes’ theorem
    Discrete and continuous probability distributions
  Students will understand the terms mean, variance, standard deviation, percentile, and be able to relate these to particular distributions used in the course

## Slide 7: Section 3: Bayesian Statistical Inference
Purpose
  Students will learn subjectivist interpretation of probability, concept of Bayesian updating, and applications to commonly encountered kinds of stochastic models
Objectives
  Students will learn
    Probability interpreted as a quantification of degree of plausibility
    Bayesian inference using Excel for
      Discrete priors
      Conjugate priors for Poisson, binomial, and exponential models
      Formal priors for Poisson, binomial, and exponential models
    RADS Calculator for conjugate and non-conjugate priors

## Slide 8: Sections 4 and 5: Uncertainty Propagation in Risk Assessment
Purpose
  Students will see an overview of how Bayesian estimates of risk metrics (e.g., core damage frequency) are obtained
Objectives
  Through examples using Excel, students will learn about
    Monte Carlo sampling of distributions
    Estimation of a “top event” probability by propagation of distributions through a logic model
    Simple Monte Carlo sampling and Latin hypercube sampling

## Slide 9: Course Reference
Handbook of Parameter Estimation for Probabilistic Risk Assessment, NUREG/CR-6823, September 2003.
  Available on NRC web site at
  www.nrc.gov/reading-rm/doc-collections/nuregs/contract/cr6823

## Slide 10: Supplemental Reference
Bayesian Inference for PRA: A Practitioner’s Guidebook, 2011
  Available at
  www.amazon.com/Bayesian-Inference-Probabilistic-Risk-Assessment/dp/1849961867
  The text for P-502

## Slide 11: Supplemental Reference
Bayesian Inference for NASA Probabilistic Risk and Reliability Analysis, NASA/SP-2009-569, 2009
  Available at
  www.hq.nasa.gov/office/codeq/doctree/SP2009569.pdf

## Slide 12: P-102 from 10,000 ft (± 2,000 ft)
Real World
Aleatory level
Epistemic level
Failure to open
Failure to close
Failure to start
Failure to run
Loss of offsite power (grid related)
Bayesian inference
Current knowledge
+
Observed data

## Slide 13: P-102 from 10,000 ft (± 2,000 ft)
Event
time
Fault-trees
Event-trees
event has NOT
occurred (1-p)
event has occurred (p)
Set of basic events
Probabilistic Risk Analysis: determine for each event
  Consequence
  Probability of occurrence
Methods: Event Trees and Fault Trees
Deduction
Induction

## Slide 14: Loss of Offsite Power (LOSP) Example
The “LOSP example” will be used as a central example throughout most of the course
A system uses offsite power, but has two standby emergency diesel generators (EDGs)
Occasionally offsite power is lost (an “initiating event”)
  When this happens the EDGs are demanded to start and run
The system
  Succeeds if either EDG starts and runs for six-hour mission time
  Fails otherwise

## Slide 15: The Concept of a Scenario
Scenario modeling
  For each hazard, identify an initiating event and necessary enabling conditions that result in undesired consequences
Enabling conditions often involve failure to recognize a hazard or failure to implement controls such as protective barriers
Accident scenario is the sequence of events comprised of:
  Initiating event + enabling conditions + events that lead to adverse consequences

## Slide 16: LOSP Example
A PRA will have an event tree representing the scenario
  Fault trees will represent the diesel generator failures
LOSP
pDG
Loss of
Offsite Power
Diesel Generator System Failure
Diesel Generator System Success
1-15

## Slide 17: Cut Sets
A Cut Set is a path to an outcome (usually we’re interested in failure)
LOSP AND DG-A-FTS AND DG-B-FTR

## Slide 18: The Minimal Cut Sets
LOSP AND DG-A-FTS AND DG-B-FTS or
LOSP AND DG-A-FTS AND DG-B-FTR or
LOSP AND DG-A-FTR AND DG-B-FTS or
LOSP AND DG-A-FTR AND DG-B-FTR

## Slide 19: Recovery of Offsite Power
Core damage can be averted if offsite power is recovered
Assume traditional engineering analysis shows…
  Recovery must occur by six hours to avert core damage
Append nonrecovery event to minimal cut sets
  This represents probability that offsite power is not recovered within six hours

## Slide 20: Recovered Cut Sets
LOSP AND DG-A-FTS AND DG-B-FTS AND OSP-NONREC or
LOSP AND DG-A-FTS AND DG-B-FTR AND OSP-NONREC or
LOSP AND DG-A-FTR AND DG-B-FTS AND OSP-NONREC or
LOSP AND DG-A-FTR AND DG-B-FTR AND OSP-NONREC

## Slide 21: “Real” PRA Cut Sets
A “real” PRA may have additional terms not considered in this class
  Common Cause Failure
  Unavailability of the component (e.g., out for test or maintenance activities)
  Human reliability
  Component recoveries